## Slide 1: Using Probe Data to Improve our Network
December 14, 2022

## Slide 2: Agenda
Define probe data used by SDOT
Describe how we verified data quality
Describe actual use cases

## Slide 3: Probe Data: Vehicle speed and travel time
Data from millions of connected vehicles from leading auto companies, including Daimler, Audi/VW, BMW, Ford, etc.
Also: GPS providers, in-vehicle navigational services, trucking companies, fleet services providers and mobile-phone companies

## Slide 4: U.S. Transportation Agencies using Probe Data to improve decision making
Maine DOT
Wisconsin DOT
Alabama DOT
Florida DOT
Utah DOT
North Carolina DOT
City of Bellevue, WA
Georgia DOT
Los Angeles Metro
New York City
Austin, TX
Boston, MA
Colorado DOT
City of Detroit
Idaho DOT
City of Las Vegas
Massachusetts DOT
Maryland DOT
City of Miami
Nevada DOT
Michigan DOT
New Jersey DOT
Arizona DOT
Washington D.C.

## Slide 5: Probe Privacy Implications
Includes no personally identifiable information
Vendors aggregate and anonymize the data before providing it to others
This solution no longer relies on license plates or other unique identifiers collected by SDOT
Per ITD privacy review, the probe data solutions do not meet definition provided in 14.18 as SDOT is only receiving a feed of data that does not include any personally identifiable information and is not analyzing the movements of specific individuals

## Slide 6: Probe Data Solution
Supports SDOT's goals of:
Equity - Data covers the entire City so we can reduce bias when prioritizing solutions
Safety - Combining speed and collision history allows a more nuanced response
Low Maintenance – used to maintain 300+ wifi sniffers in signal cabinets, a data feed only needs a web browser
Probe Data: real-time data from connected vehicles, GPS and navigation devices.
Notes: Car Icon is CC By OliM, FR

## Slide 7: Check the Data Quality
Data are only as good as it’s understood and accepted
Travel Time comparison
  Floating car
Speed comparison
  Pneumatic tubes

## Slide 8: Travel Times
  Seven vendor solutions compared with a floating car on four Seattle arterials
  Each dataset responds differently to traffic slowdowns
"Performance on the slowdown analysis – the current preferred way to quantify operational performance on arterials – improved dramatically" when comparing probe data from 2013 to 2018.​
-University of Maryland Vehicle Probe Project
Notes: https://tetcoalition.org/wp-content/uploads/2015/02/I-95-CC-Validation_Arterials_Report-Sep2019-Final.pdf

## Slide 9: Speed Comparison – urban highway NB, N/O Aurora Bridge
  Probe data: 900 foot long “segment speed”
  Tube: “spot speed”
  85th Percentile speeds averaged 6 MPH less on probe than tube
Notes: Note hole in tube data with tube up – all data has issues
Note probe data slower over segment speed

## Slide 10: Speed Comparison – dense neighborhood SB, Queen Anne Ave N, N/O John St
  Probe: 422 foot long “segment speed”
  Tube: “spot speed”
  15th and 50th percentile speeds quite different
  85th Percentile speeds averaged 4 MPH less on probe than tube
Notes: 2 SB only lanes

## Slide 11: Check the Data Quality
Data are only as good as it’s understood and accepted
Travel Time comparison
  Found dataset that generally matched a floating car
Speed comparison
  85th percentile usually about 5 MPH less than spot speeds

## Slide 12: Use Cases
  VZ: High Speed Ratio
  Understand the relationship between posted and actual speeds.
  Reliability Index
  Measure the extent of unexpected delays.
  Before/After Analysis
  Review behaviors before and after changes are made.
  DMS Travel Times
  Communicate with the public.
Notes: Not listed – grant proposals – easier to quantify the problem

## Slide 13: Use Case: Inform the Public
38 Dynamic Message Signs
  2-4 travel times per sign
  Real-time updates
  Flexible routing
  Reliable data
Notes:   Updated every minute
  Travel times can be measured exactly where we need them, not dependent on installing sensors
  Highly reliable data flow, no longer reliant on physical sensors working

## Slide 14: Vision Zero: Lower Speeds to Save Lives
Full knowledge of vehicle speeds, citywide enables equitable decisions
Can compare to speed limits and our collision data to target Vision Zero efforts

## Slide 15: Use Case: Monitor Reliability, Weekly Report
West Seattle Bridge Closed
  How are the detour routes working out?
  Planning time: 95th percentile
  Typical time: median

## Slide 16: Use Case: Before/After Study Clear Traffic After Large Events
Full knowledge of vehicle speeds
Can pinpoint slowdowns
Evaluate different traffic management plans
Post Seahawks Game
Notes: Entering in a partnership with Google to see if they can recommend changes – this data will be key in measuring success in any testing

## Slide 17: Use Case: Investigate Constituent Concerns
Before/After evaluation possible on all arterials, anytime
NE 55th St between 33rd Ave NE and 28th Ave NE
Weekdays, no holidays, January 2022
7 AM to 10 PM
Speed limit: 25 MPH

## Slide 18: Use Case: Investigate Constituent Concerns
Alki Ave in West Seattle –complaints of summer speeding
Notes: Speed humps now installed

## Slide 19: Thank You Jeffrey Conor Jeffrey.Conor@seattle.gov